Vinebot run instruction:

switch on the laptop with ubuntu 20.04 and launch files of the vinebotand rtabmap

1. Connect the main power supply of the Vinebot using the red connector, connect the usb of the vinebot to the usb of the PC.
2. rgbd cam mapping instructions(switch on mapping node)

roslaunch realsense2_camera opensource_tracking_vinebot.launch

vinebot launch files

3. Run the ROS Master on your current terminal using the command below, which will launch the Vinebot ROS software on your laptop

roslaunch roboteq_control bringup.launch

4. control with joystick:
6. In order to connect the PS4 joystick use the following instruction:
6.1. Connect you joystick to your computer through the Bluetooth connection.
6.2. Open new terminal and run su root:
$sudo su root
6.3. Once you have sudo access, run the following ds4drv driver:
$ds4drv --hidraw
6.4. If you have done all steps up to this, you should see the created joystick controller on	your terminal. (ex. Created devices /dev/input/js1 (joystick) /dev/input/event16 (evdev)). If	you see this message, you are ready to launch ROS driver to send the joystick values to	corresponding topics to control the Vinebot remotely.

alternative ps4 approach
$ds4drv if it is not running already.
1. rosparam set joy_node/dev "/dev/input/js1"
2. rosrun joy joy_node
3. rosrun ps4_ros ps4_ros
note: before moving the vinebot, calibrate the joystick and release the emergency stop (check both switches)

rgbd saving instructions
after mapping is completed
rosrun pcl_ros pointcloud_to_pcd input:=/rtabmap/cloud_map
rosrun map_server map_saver map:=/rtabmap/proj_map

saving the db file in a new folder
location if the db file : .ros/rtabmap.db
save the map files in a new directory
for LOCALIZATION
roslaunch realsense2_camera opensource_tracking_vinebot_localization.launch
roslaunch realsense2_camera opensource_tracking_vinebot_localization_rtabrviz.launch

livox mapping
roslaunch livox_mapping mapping_mid.launch
roslaunch livox_ros_driver livox_lidar.launch