Vinebot run instruction:

1. Connect the main power supply of the Vinebot using the red connector, make sure all the equipment are powered on. (etc. modem, raspberry pi, motor controller).
2. Check the Roboteq motor controller mode, the right LED light must peak only once in 3 seconds, which means it is working on serial connection mode. Ensure the controller works within the specified ambient temperature range.

3. Run the Ubuntu OS on your control station computer, make sure you have all the Vinebot packages on both side of stations. Then, get connected to the router located on the Vinebot, which has the name “dlink”(normally, it has no password).
4. Open the terminal on your computer and connect to the on-board raspberry pi using the following ssh command: $ssh ubuntu@192.168.0.100.
If the connection is successful you should see the welcome message and some information about the raspberry.

5. Run the ROS Master on your current terminal using the command below, which will launch the Vinebot ROS software on your raspberry pi.
$roslaunch roboteq_control bringup.launch

6. In order to connect the PS4 joystick use the following instruction:
6.1. Connect you joystick to your computer through the Bluetooth connection.
6.2. Open new terminal and run su root:
$sudo su root
6.3. Once you have sudo access, run the following ds4drv driver:
$ds4drv --hidraw
6.4. If you have done all steps up to this, you should see the created joystick controller on	your terminal. (ex. Created devices /dev/input/js1 (joystick) /dev/input/event16 (evdev)). If	you see this message, you are ready to launch ROS driver to send the joystick values to	corresponding topics to control the Vinebot remotely.
6.5. Then launch the Sony PlayStation 4 DualShock®4 node using the following command on new ubuntu terminal:
$ roslaunch ps4_ros ps4.launch

alternative ps4 approach
$ds4drv if it is not running already.
1. rosparam set joy_node/dev "/dev/input/js1"
2. rosrun joy joy_node
3. rosrun ps4_ros ps4_ros

rgbd cam instructions

roslaunch realsense2_camera opensource_tracking_vinebot.launch
rosrun pcl_ros pointcloud_to_pcd input:=/rtabmap/cloud_map
rosrun map_server map_saver map:=/rtabmap/proj_map

livox mapping
roslaunch livox_mapping mapping_mid.launch
roslaunch livox_ros_driver livox_lidar.launch